## Slide 1
RT 524 – Digital Agriculture and Advanced Analytics
Fully Wireless Sensor with NodeMCU
Submitted by:
Shivani Agrawal (254154007) & Vivek Sharma(256154006)
School of Agro and Rural Technology (SART)
IIT Guwahati (781039)
Submitted to:
Dr. Dipankar Mandal
Assistant Professor
Mini Project

## Slide 2
Circuit Connections — Fritzing Diagram
​1. FC-28 Soil Moisture Probe
​It consists of two large exposed pads that act as variable resistors.
​How it works: When the soil is wet, it conducts electricity more easily (lower resistance). When the soil is dry, it conducts poorly (higher resistance).
​2. Soil Moisture Control Module (Comparator) ​This is the small blue board connected directly to the FC-28 probe. It processes the raw signal from the probe before sending it to the microcontroller.
​3. NodeMCU ESP8266 ​The large black board in the centre is the “brain” of the project. It is a Wi-Fi-enabled microcontroller based on the ESP8266 chip. ​Function: It reads the data from the sensors, processes the values, and can transmit that data over Wi-Fi to a phone app or a cloud dashboard.
​4. DHT11 Temperature & Humidity Sensor ​The small blue grid-like component on the right is a DHT11 sensor. ​Function: Unlike the FC-28 which measures the ground, this measures the ambient air. It provides two readings: temperature and relative humidity.

## Slide 3
Project Overview
🎯 Objective
Build a fully wireless sensor system using NodeMCU (ESP8266) to monitor soil moisture and ambient temperature & humidity in agricultural fields.
🔌 Key Components
NodeMCU ESP8266 • FC-28 Soil Moisture Sensor • DHT11 Temperature & Humidity Sensor
📡 What Makes it Wireless
NodeMCU has built-in WiFi (ESP8266 chip). Sensor data can be transmitted over WiFi for remote monitoring and data logging.
📊 Output
Real-time sensor readings displayed in Arduino Serial Monitor at 115200 baud. Values: Soil Moisture %, Temperature °C, Humidity %.

## Slide 4
Pin Connection Details
FC-28 Soil Moisture Sensor → NodeMCU
Sensor Pin | NodeMCU Pin | Purpose
AO (Analog Out) | A0 | Analog moisture reading
VCC | VIN | Power supply
GND | G | Ground
Sensor Pin NodeMCU Pin Purpose
DHT11 Temperature & Humidity Sensor → NodeMCU
Sensor Pin | NodeMCU Pin | Purpose
VCC | 3V | Power supply
GND | GND | Ground
DATA | D4 (GPIO2) | Temperature & Humidity data
Sensor Pin NodeMCU Pin Purpose

## Slide 5
Step 1 — Install Silicon Labs CP210x USB to UART Bridge Driver
Why is this needed?
NodeMCU uses a CP210x chip to convert USB signals to UART (serial). Without the driver, your computer cannot detect or communicate with the NodeMCU board.
1
Download Driver
Visit Silicon Labs website → search 'CP210x USB to UART Bridge VCP Drivers'. Download for your OS (Windows / Mac / Linux).
2
Run Installer
Extract the zip file. Run the .exe (Windows) or .dmg (Mac). Follow the installation wizard and complete setup.
3
Connect NodeMCU
Plug NodeMCU to computer via Micro-USB cable. Windows: Check Device Manager → Ports (COM & LPT). A new COM port should appear.
4
Verify Detection
On Windows: Device Manager → Ports → 'Silicon Labs CP210x USB to UART Bridge (COMx)'. This confirms driver is working correctly.

## Slide 6
Step 2 — Install Libraries in Arduino IDE
Two libraries must be installed to use NodeMCU's WiFi and DHT sensor features:
📶 ESP8266WiFi.h
Purpose: Gives NodeMCU its WiFi superpowers. How to install: Arduino IDE → Tools → Manage Libraries → search 'ESP8266WiFi' → Install Package: Part of ESP8266 board package by esp8266 community
🌡 DHT.h (DHT sensor library)
Purpose: Enables reading from DHT11/DHT22 sensors. How to install: Arduino IDE → Tools → Manage Libraries → search 'DHT sensor library' by Adafruit → Install Note: Also install 'Adafruit Unified Sensor' if prompted
📌 How to Add ESP8266 Board to Arduino IDE
1. File → Preferences → Paste this URL in 'Additional Boards Manager URLs':
http://arduino.esp8266.com/stable/package_esp8266com_index.json
3. Tools → Board → Boards Manager → search 'esp8266' → Install 'esp8266 by ESP8266 Community'

## Slide 7
Step 3 — Select Board & Port in Arduino IDE
🖥️ Select the Board
Go to: Tools → Board → ESP8266 Boards → select 'NodeMCU 1.0 (ESP-12E Module)'. This tells Arduino IDE which microcontroller you are using.
▶ Tools → Board → ESP8266 Boards → NodeMCU 1.0
🔌 Select the Port
Go to: Tools → Port → Select the COM port where NodeMCU is connected. On Windows it appears as COM3, COM4, etc.
▶ Tools → Port → COMx
⚙️ Upload Speed
Tools → Upload Speed → 115200. This matches the Serial.begin(115200) in your code. Mismatched baud rates cause garbled output in monitor.
▶ Tools → Upload Speed → 115200
✅ Verify Selection
Bottom bar of Arduino IDE shows current board & port. Example: 'NodeMCU 1.0 (ESP-12E Module) on COM4'. Now you are ready to upload code.
▶ Bottom bar → NodeMCU 1.0 on COMx

## Slide 8
Setting of baud rate in serial monitor to 115200:
Selection of Board and port in Arduino IDE:

## Slide 9
Step 4 — Write Code

## Slide 10
Including Libraries in the Code
Every Arduino sketch begins by importing the libraries it needs. Here's what each line does:
#include <ESP8266WiFi.h>
#include <DHT.h>
ESP8266WiFi.h
Activates WiFi features for NodeMCU (ESP8266). This library contains all functions needed to connect your board to the internet — scanning networks, connecting, sending data, and more. Without this line, your NodeMCU is just a regular Arduino with no wireless capability.
DHT.h
Adds support for DHT family sensors (DHT11, DHT22, DHT21). Provides easy functions:
• dht.readTemperature() → returns °C
• dht.readHumidity() → returns %
// DHT Sensor Configuration
#define DHTPIN D4
#define DHTTYPE DHT11
DHT dht(DHTPIN, DHTTYPE);

## Slide 11
DHT Sensor Configuration in Code
Line-by-line explanation of DHT11 sensor setup:
#define DHTPIN D4
Define DHT Data Pin
This tells the program: 'DHT sensor's data wire is connected to D4 on NodeMCU'.
#define DHTTYPE DHT11
Define Sensor Type
Specifies which DHT model you are using. DHT11 is the basic blue sensor.
DHT dht(DHTPIN, DHTTYPE);
Create DHT Object
Creates a controller named 'dht' for your sensor. Think of it as registering your sensor: telling the code which pin it's on and what type it is.

## Slide 12
Soil Moisture Sensor Configuration
The FC-28 soil sensor outputs an analog voltage. NodeMCU reads it on pin A0 (the only analog input).
#define SOIL_PIN A0
int dryValue = 800;
int wetValue = 300;
#define SOIL_PIN A0
Defines the analog pin A0.
Soil sensor gives analog voltage.
NodeMCU has only ONE analog pin (A0), so the soil sensor must always use A0.
dryValue = 800
When soil is completely DRY, the sensor outputs ~800 (raw ADC value). This is the reference for 0% moisture.
wetValue = 300
When soil is WET/soaked, sensor outputs ~300. This is the reference for 100% moisture.
Values are inverted — lower = wetter.
Why Calibrate?
Different soils & sensors have different raw ranges. Calibration maps raw numbers (300–800) to readable % (0–100) for humans.

## Slide 13
The setup() Function
Runs ONCE when the board powers on. Initializes everything before the main loop begins.
void setup() {
Serial.begin(115200);
delay(1000);
Serial.println("Wireless Soil & Humidity Sensor
Starting..."
);
dht.begin();
}
Start Serial Communication
Opens a communication channel between NodeMCU and your computer at 115200 bps. This is required to see output in the Serial Monitor.
Wait 1 Second
Gives the system time to stabilize after power-on. Prevents sensor reading errors immediately after startup.
Print Startup Message
Sends a startup confirmation to Serial Monitor. Useful for debugging — confirms the board is running your code.
Initialize DHT Sensor
Starts the DHT11 sensor. Without this, all calls to dht.readTemperature() and dht.readHumidity() will return NaN (error).

## Slide 14
The loop() Function & Reading Soil Moisture
The loop() function runs forever, continuously reading and printing sensor data:
void loop() {
int soilRaw = analogRead(SOIL_PIN);
int soilPercent = map(soilRaw,dryValue,wetValue,0,100);
soilPercent = constrain(soilPercent, 0, 100);
Read Raw Soil Value
Reads analog voltage on A0 (0–1023). Wet soil → ~300. Dry soil → ~800. The value represents electrical conductivity of soil.
Convert Raw to Percentage
map() translates one number range to another. 800 becomes 0%, 300 becomes 100%.
Clamp to Valid Range
Prevents out-of-range values (-5%, 120%) caused by extreme conditions. Forces: minimum = 0%, maximum = 100% always.

## Slide 15
Reading Temperature & Humidity (DHT11)
float humidity = dht.readHumidity();
float temperature = dht.readTemperature();
if (isnan(humidity) ||
isnan(temperature)) {
Serial.println("Error!");
return;
}
dht.readHumidity()
Returns relative humidity as a float (e.g. 65.5%). Stored as 'float' because the sensor gives decimal precision. Range: 20–90% RH for DHT11.
dht.readTemperature()
Returns temperature in Celsius as a float (e.g. 28.3°C). Range: 0–50°C for DHT11. Use readTemperature(true) for Fahrenheit.
isnan() — Check for Errors
DHT sensors sometimes fail to read and return NaN (Not a Number). isnan() detects this. If error detected → print message + return (skip rest of loop).

## Slide 16
Step 5 — Setting Baud Rate to 115200 in Serial Monitor
Baud rate is the speed of communication between NodeMCU and your computer.
📟 What is Baud Rate?
Baud rate = bits per second (bps). 115200 means 115,200 bits are transmitted per second. It controls how fast data flows from NodeMCU to Arduino Serial Monitor.
⚠️ Why Must They Match?
Code uses Serial.begin(115200). Serial Monitor must also be set to 115200.
🔧 How to Set in Serial Monitor
Open Serial Monitor: Tools → Serial Monitor (or Ctrl+Shift+M). Bottom-right dropdown → select '115200 baud'.
✅ What You'll See (Correct Output)
Wireless Soil & Humidity Sensor Starting...
Soil Moisture: 62%
Temperature: 28.30°C
Humidity: 65.10%
---

## Slide 17
Step 6 — Result
Expected Serial Monitor output and sensor behavior during testing:
📟 Serial Monitor Output (115200 baud)

## Slide 18
THANK YOU